# Comparison of 2 THD algorithms
Alg. 1: TWM-THDWFFT, based on windowed FFT,
Alg. 2: TWM-MFSF, based on Multi Harmonic Frequency Estimator.
## Testing signal properties
Nominal values:
    fs.v = 1e5; fs.u = 1e-9; % is it used somewhere?
    % record length:
    L.v = 1e5;
    % signal frequency
    f.v = 50.01; f.u = 0.01; % this is uncertainty of estimate. is it used in some alg?
    % harmonics
    DI.nharm.v = [1 2 3 4 5]; % signal harmonic multiple
    DI.A.v = [1 0.01 0.01 0.01 0.01]; % signal amplitudes
    DI.ph.v = [0 0 0 0 0]; % signal phase
    DI.O.v = [0 0 0 0 0]; % signal offset
    DI.noise.v = 1e-5;
# Variation: noise
DIvar.noise.v = logspace(-6, 1, 20);

## Variation: THD value
DIvar.A.v = logspace(-6, -2, 10)'.*[1 1 1 1];
DIvar.A.v = [ones(size(DIvar.A.v,1), 1) DIvar.A.v];
that results in reference THD values:
ans =   2.0000e-04   5.5651e-04   1.5485e-03   4.3089e-03   1.1990e-02   3.3362e-02   9.2832e-02   2.5831e-01   7.1876e-01   2.0000e+00

## Variation: frequency
DIvar.f.v = 50 + [-0.5:0.0001:0.5];
(guf)